## Slide 1
A Hybrid TCN-BiLSTM Framework for Noise-Robust Multi-Class Motor Fault Diagnosis Using Vibration Spectrograms
Anil Kadu, Anup Deshmukh, Akshad Bharate, Vivek Chaudhari, Mohan Navbade
Department of Instrumentation and Control Engineering
Vishwakarma Institute of Technology, Pune, Maharashtra, India

## Slide 2
Bridging the Gap Between Laboratory Diagnostics and Industrial Realities
~70%
Electric motors consume roughly 70% of total industrial electricity usage in the US. Unexpected failures cause severe productivity losses and soaring maintenance costs.
Controlled Laboratory Diagnostics
Current data-driven deep learning models perform exceptionally well in controlled laboratory settings under standardized operating conditions and constant loads.
Real-World Industrial Challenges
Models frequently fail when deployed in real-world environments due to varying load conditions, significant background operational noise, and complex overlapping spectra from simultaneous compound faults.
Our Focus: Our work addresses this critical gap by prioritizing realistic noise robustness in deep learning architectures for reliable industrial deployment.

## Slide 3
Three Pillars for Robust Motor Fault Diagnosis
account_tree
Hybrid Architecture
We introduce a novel TCN-BiLSTM framework that combines multi-scale temporal feature extraction with bidirectional sequence modeling for four-class fault diagnosis.
folder_special
Strict File-Wise Partitioning
We designed a robust data splitting scheme that completely prevents inter-session information leakage, ensuring our evaluation strictly mimics actual deployment realities.
graphic_eq
Realistic Noise Robustness
We conducted a comprehensive evaluation under clean-only, noise-only, and mixed training regimes using actual recorded industrial noise rather than artificial data augmentations.

## Slide 4
SOON-PeMP Dataset & Leak-Free Protocol
Dataset Overview: Utilized 30 independent recording sessions covering 4 health states (normal, mechanical failure, electrical failure, compound faults).
Partitioning Strategy: Applied strict file-wise allocation to completely eliminate data leakage across sets, avoiding random shuffling.
70%
Training Partition
Training Set
• Allocation: 21 Recording Files
• Volume: 1,215 Instances
Isolated recording sessions strictly dedicated to model training.
15%
Validation Partition
Validation Set
• Allocation: 5 Recording Files
• Volume: 246 Instances
Independent sessions utilized strictly for hyperparameter tuning.
15%
Testing Partition
Testing Set
• Allocation: 4 Recording Files
• Volume: 216 Instances
Completely unseen recording sessions for unbiased evaluation.

## Slide 5
Extracting Joint Time-Frequency Features via STFT
Motor vibration signals are highly non-stationary. To capture these complex temporal patterns, raw vibration sequences are converted into normalized Short-Time Fourier Transform (STFT) spectrograms, preserving both time and frequency information for downstream analysis.
STFT Parameter Setup
• Window: Hann (1,024 samples)
• Overlap: 50% shift
• Sampling Freq: 50 kHz
STFT Data Processing Pipeline
Step 01
Raw Vibration Signal
50 kHz sampling rate input sequences
Step 02
STFT Resolution
48.8 Hz res. resolves 50–300 Hz harmonics
Step 03
dB Scaling & Norm.
Logarithmic decibel conversion
Output
511 × 32 Map
Fixed Time-Freq feature matrix
* Note: The selected window size prevents loss of temporal resolution while maintaining strict harmonic isolation required for fault diagnostics.

## Slide 6
A Lightweight Hybrid TCN-BiLSTM Network Architecture
Input Layer
STFT Input
511-D Spectral
32-Frame Sequence
Feature Extraction
Dilated TCN
Dilation: 1, 2, 4
Multi-scale Features
Temporal Context
BiLSTM
64-D Vector Input
128 Units / Direction
Output Stage
Dense Layers
Dropout Regularization
4-Class Output
511 Dimensions
Reduced to 64-D
Forward/Backward Context
Final Probability
Model Scale
~1.2M
Trainable Parameters
Ensures high computational efficiency for real-time deployment.
Multi-Scale Feature Extraction: Stacked dilated Temporal Convolutional Networks (TCNs) extract broad temporal receptive fields using dilation rates of 1, 2, and 4.
Contextual Dependency Learning: A Bidirectional LSTM with 128 hidden units per direction captures comprehensive forward and backward dependencies across 32-frame sequences.
Dimensionality Reduction & Regularization: Reduces high-dimensional (511-D) spectral inputs down to 64-D before final fully connected layers and dropout for four-class classification.

## Slide 7
Architectural Ablation Validates the Hybrid Approach
We conducted a comprehensive ablation study using identical file-wise splits to isolate architectural contributions. Evaluation reveals that combining TCN's multiscale feature extraction with BiLSTM's temporal context yields optimal performance under the clean-trained evaluation protocol.
22.73%
BiLSTM-Only Model
Struggled with high-dimensional inputs
83.43%
Standard CNN-LSTM
Lacked long-term temporal reach
91.36%
TCN-Only Architecture
Multiscale filters; missed bidirectional context
95.45%
Proposed TCN-BiLSTM
Outperformed all baselines (0.964 Macro F1)
Key Takeaway: The proposed hybrid TCN-BiLSTM architecture effectively resolves long-range dependencies and multiscale spectral feature integration, achieving state-of-the-art accuracy.

## Slide 8
Advancing Reliable and Deployable Motor Condition Monitoring
99.55%
Overall Accuracy
The TCN-BiLSTM framework successfully bridges the gap between laboratory and industrial fault diagnosis. By training on mixed conditions with real background noise, the model achieves a remarkable 99.55% overall accuracy. The strict file-wise splitting protocol ensures these results reflect realistic deployment capabilities.
Future Research Directions
Cross-Dataset Validation
Conduct extensive cross-dataset validation on CWRU and Paderborn benchmarks to evaluate model generalizability across diverse operating environments.
Model Interpretability
Integrate Grad-CAM techniques for interpretability and visual explainability of deep learned representations and decision boundaries.
Edge IoT Deployment
Optimize the lightweight 1.2 million parameter model for efficient edge deployment on resource-constrained embedded IoT hardware.

## Slide 9
Conclusion & Deployment Roadmap
“The hybrid framework provides lightweight, noise-robust diagnosis, paving the way for edge deployment.”
Architecture & Latency Benchmarks
The TCN-BiLSTM architecture successfully addresses the complementary limitations of purely convolutional and recurrent models. Inference latencies of 1.8 ms on GPU and 12.4 ms on CPU confirm its suitability for real-time PC-side condition monitoring.
Future IoT Edge Deployment Roadmap
Future work will focus on cross-dataset validation using CWRU and Paderborn benchmarks, the integration of Grad-CAM-based explainability for feature maps, and quantized deployment on embedded IoT hardware such as STM32 or ARM Cortex-M platforms.